## Slide 1: Heat Engines
forward and backward
§ 12.4

## Slide 2: Heat Engines
Divert heat flow

## Slide 3: Heat Engine
Heat flow can be diverted to useful work
Qh
Qc
W
Th
Tc
Qh = W + Qc
As long as entropy still increases
Qc/Tc ≥ Qh/Th

## Slide 4: Rankine cycle (Steam engine)
Low-pressure water is compressed
p
V
Heated to steam at constant pressure
  doing work
Expanded adiabatically to its initial pressure
  doing more work
Cooled at constant pressure to its initial temp
  expelling waste heat

## Slide 5: Carnot cycle
Compress a gas adiabatically
  increase p, T
p
V
Allow to expand isothermally
  High T
  with heat input
Allow to expand adiabatically
  decrease p, T
Compress isothermally
  Low T
  expelling waste heat

## Slide 6: Heat Engine
Efficiency = e
One type of performance
Th
Qh
Qc
W
Tc
e = W /Qh

## Slide 7: Limits to Efficiency
e = W /Qh
= (Qh–Qc)/Qh
= 1 – Qc/Qh
now
Qc/Tc ≥ Qh/Th, so Qc/Qh ≥ Tc/Th
thus
e ≤ 1 – Tc/Th

## Slide 8: Refrigerators and Heat Pumps
push heat upstream

## Slide 9: Devices
Refrigerator
  Removes heat from interior, lowering the temperature
  Goal: keep interior colder than exterior
Heat Pump
  Transfers heat from cold surrounding to warm interior
  Goal: keep interior warmer than exterior

## Slide 10: Heat Pump or Refrigerator
Heat flows uphill!
Still, entropy must increase
Th
Tc
Qh = W + Qc
Qh/Th ≥ Qc/Tc
Qh
Qc
W

## Slide 11: Performance of a Refrigerator
We want Qc, must provide W
COP = Qc/W
Th
Tc
Qh
Qc
W

## Slide 12: Refrigerator Performance Limits
COP = Qc/W
= Qc/(Qh–Qc)
now
Qh/Th ≥ Qc/Tc, so
(Qc + W)Tc ≥ QcTh
WTc ≥ Qc(Th – Tc)
Tc/(Th–Tc) ≥ Qc/W
thus
COP ≤ Tc/(Th–Tc)

## Slide 13: Performance of a Heat Pump
We want Qh, must provide W
COP = Qh/W
Th
Tc
Qh
Qc
W

## Slide 14: Heat Pump Performance Limits
COP = Qh/W
= Qh/(Qh–Qc)
now
Qh/Th ≥ Qc/Tc, so
QhTc ≥ QhTh – WTh
WTh ≥ Qc(Th – Tc)
Th/(Th–Tc) ≥ Qc/W
thus
COP ≤ Th/(Th–Tc)