## Slide 1: Voltage
Absolute potential is seldom important
Potential difference is what matters
Voltage ≡ potential difference

## Slide 2: Capacitors
A device storing electrical energy

## Slide 3: Capacitor
Device storing electric potential energy
Positive charge accumulates in one place, Negative charge accumulates in another
Voltage is proportional to charge separated
V=Q/C

## Slide 4: Capacitor
A voltage between connected plates causes charge migration until equilibrium
DV
– –
– –
– –
–
+ +
+ +
+ +
+
–Q
+Q
Charge stored Q = CV
C = capacitance
(property of the device)
Unit = C/V = farad= F

## Slide 5: Parallel Plate Capacitance
Plate area A, separation d
d
A
Capacitance = Ae0/d
e0 = 8.8510–12
C2
N m2

## Slide 6: Field Around Infinite Plate
With uniform charge density s = Q/A
FE =
sA
e0
s
e0
1
2
, so E =
= E(2A)

## Slide 7: Infinite ||-Plate capacitor
Individually
–s
1/2 s/e0
+s
1/2 s/e0
+s
−s
s/e0
0
0
Together

## Slide 8: Infinite ||-Plate capacitor
Voltage between plates
+s
−s
s/e0
0
0
d

## Slide 9: Finite ||-Plate Capacitor
Parallel plates of charge Q, area A, spacing d
Charge density s = Q/A
–Q
+Q
Fields cancel outside
Fields cancel outside
d
Voltge
Capacitance C = Q/V
s/e0
constant!

## Slide 10: Parallel Plate Capacitance
Plate area A, plate separation d
Field E =
s
e0
=
Q
Ae0
Potential DV = Ed =
Qd
Ae0
Capacitance Q/DV =
Q Ae0
Qd
Ae0
d
=

## Slide 11: Circuit Element Symbols
Potential Source
+ –
DV
Conductor
Capacitor
or
Resistor

## Slide 12: At Equilibrium
DV
C
+ –
Capacitor charges to potential V
Capacitor charge Q = CV
+ –
V

## Slide 13: Energy in a Capacitor
C = Q/V so V = Q/C
V
Q
Work to push charge Q dW = VdQ = (Q/C)dQ
slope = 1/C
dQ
area = dW

## Slide 14: Energy in a Capacitor
Work to charge to Q is area of triangle W = 1/2 Q(Q/C) = 1/2 Q2/C
V
Q
Q/C
CDV
Work to charge to V W = 1/2 V (CV) = 1/2 C(V)2

## Slide 15: Combining Capacitors
and
Parallel
Series

## Slide 16: Parallel Components
All have the same potential difference
Capacitances add
(conceptually add A’s)

## Slide 17: Series Capacitors
All have the same charge separation
Reciprocals of C are additive
(conceptually add d’s)

## Slide 18: Capacitor with a Dielectric
If capacitance without dielectric is C, capacitance with dielectric is kC.
k = dielectric constant
k

## Slide 19: Dielectric
Insulator
Polarizes in field
Effectively reduces plate separation d
Reduces field between plates
Dielectric constant = relative permittivity e = ke0
Capacitance C = Ae/d

## Slide 20: Dielectric breakdown
Strong field can separate charges
  Ejects electrons from their orbitals
Dielectric becomes a conductor
Damage usually permanent
Limits practical thinness of dielectric layer

## Slide 21: Some Dielectrics
Material | k | Strength (kV/mm)
Air | 1.0006 | 3
Paper | 3.85 | 16
Teflon | 2.1 | 19.7
Mica | 3–6 | 118
TiO2 | 86–173 | 4
Silica | 4 | 470–670